#include <stdio.h>
#define MAX_TEMP (70.0)
#define MIN_TEMP (66.0)
#define CHATTER_LIMIT (2)

#define NO_HEAT 1
#define NORMAL_HEAT 2
#define FAST_HEAT 3

int controller(double room_temp){
static int on_ctr, off_ctr, chatter_detect_ctr;
static int previous_command, command, u;

if (room_temp >= MIN_TEMP && room_temp < MAX_TEMP)
command = NORMAL_HEAT;
else if (room_temp >= MAX_TEMP)
command = NO_HEAT;
else if (room_temp < MIN_TEMP)
command = FAST_HEAT;
else
command = previous_command;

if (off_ctr >= 5 || on_ctr >= 5)
chatter_detect_ctr=0;

if (command != previous_command)
chatter_detect_ctr++;

if (chatter_detect_ctr > CHATTER_LIMIT)
command = previous_command;

if (command == NO_HEAT){
on_ctr=0;
off_ctr++;
} else {
on_ctr++;
off_ctr=0;
}

if (command==NO_HEAT)
u = 20;
if (command==FAST_HEAT)
u = 100;
if (command==NORMAL_HEAT)
u = 70;

return u;
}

=========== End of the Controller Program ===========

/*----Control Variables-------SSA/SMT Variables ------------*/
/*----------------------------------------------------------*/
on_ctr
off_ctr
chatter_ctr
cmd	cmd_k_i
u
/*----State Variables-------SSA/SMT Variables ------------*/
/*----------------------------------------------------------*/
room_temp
/*------------------- Part - 1 -----------------------*/
/*------------ of Original Control Program -----------*/

if(room_temp >= MED_TEMP && room_temp < MAX_TEMP)
    command_to_heater = 2;
else if(room_temp >= MAX_TEMP)
    command_to_heater = 0;
else if(room_temp < MED_TEMP)
      command_to_heater = 1;
else
    command_to_heater = previous_command_to_heater;

/*------------------- SSA Conversion of Original Control Program ------------*/

command_to_heater_0_1 = (room_temp_0_t >= MED_TEMP && room_temp_0_t < MAX_TEMP) ?
2 : ( (room_temp_0_t >= MAX_TEMP) ?
0 : ( (room_temp_0_t < MED_TEMP) ?
1 : command_to_heater_0_0) )
/*------------------- SMT Conversion-----------*/

(ite (and (>= room_temp_0_t 66.00) (< room_temp_0_t 70.00)) (= command_to_heater_0_1 2)
 ((ite (>= room_temp_0_t 70.00) (= command_to_heater_0_1 0)
 ((ite (< room_temp_0_t 66.00) (= command_to_heater_0_1 1)
 (= command_to_heater_0_1 command_to_heater_0_0))))))
/*-----------------------------------------------------*/

/*------------------- Part - 2 -----------------------*/
/*------------ of Original Control Program ------------*/

if(off_counter >= 5 || on_counter >= 5)
    chatter_detect = 0;

if(command_to_heater != previous_command_to_heater)
    chatter_detect++;

if(chatter_detect > chatter_limit)
    command_to_heater = previous_command_to_heater;

/*------------------- SSA Conversion of Original Control Program -----------------*/

chatter_detect_0_1 =	(off_counter_0_0 >= 5 || on_counter_0_0 >= 5) ?
    0 : chatter_detect_0_0

chatter_detect_0_2 =	(command_to_heater_0_1 != command_to_heater_0_0) ?
    (chatter_detect_0_1 + 1) : chatter_detect_0_1

command_to_heater_0_2 = (chatter_detect_0_2 > chatter_limit) ?
command_to_heater_0_0 : command_to_heater_0_1
/*----------------------------------------------------------*/
/*------------------- SMT Conversion -----------------*/
(ite (or (>= off_counter_0_0 5) (>= on_counter_0_0 5)
 (= chatter_detect_0_1 0)
 (= chatter_detect_0_1 chatter_detect_0_0)))

(ite (or (> command_to_heater_0_1 command_to_heater_0_0)
 (< command_to_heater_0_1 command_to_heater_0_0))
 (= chatter_detect_0_2 (chatter_detect_0_1 + 1) )
 (= chatter_detect_0_2 chatter_detect_0_1 ) )

(ite (> chatter_detect_0_2 2)
 (= command_to_heater_0_2 command_to_heater_0_0)
 (= command_to_heater_0_2 command_to_heater_0_1))
/*----------------------------------------------------------*/

/*------------------- Part - 3 -----------------------*/
/*------------ of Original Control Program ------------*/
if(command_to_heater == 0)
  {
    on_counter = 0;
    off_counter++;
  }
  else
  {
    on_counter++;
    off_counter = 0;
}
/*------------------- SSA Conversion of Original Control Program -----------------*/
on_counter_0_1 = (command_to_heater_0_2 == 0) ?
0 : (on_counter_0_0 + 1)

off_counter_0_1 = (command_to_heater_0_2 == 0) ?
 (off_counter_0_0 + 1) : 0
/*------------------- SMT Conversion -----------------------*/
(ite (= command_to_heater_0_2 0)
 (and (= on_counter_0_1 0)
 (= off_counter_0_1 (+ off_counter_0_0 1)))
 (and (= on_counter_0_1 (+ on_counter_0_0 1))
 (= off_counter_0_1 0)))

/*------------------- Part - 4 -----------------------*/
/*------------ of Original Control Program ------------*/
if(command_to_heater == No_Heat)	u = 20;
else if(command_to_heater == Fast_Heat)	u = 100;
else if(command_to_heater == Normal_Heat)	u = 70;
else	u = u; //No change
/*----------------------------------------------------------*/
/*------------------- SSA Conversion of Original Control Program -----------------*/
u_0_1 = (command_to_heater_0_2 == 0) ?
20 : ((command_to_heater_0_2 == 1) ?
100 : (command_to_heater_0_2 == 2) ?
70 : u_0_0 )
/*------------------- SMT Conversion -----------------*/
(ite (= command_to_heater_0_2 0)
 (= u_0_1 20)
 (ite (= command_to_heater_0_2 1)
 (= u_0_1 100)
 (ite (= command_to_heater_0_2 2)
 (= u_0_1 70)
 (= u_0_1 u_0_0))))
 /*------------------- SMT Assignments -----------------------*/
(= command_to_heater_1_0 command_to_heater_0_2) (= off_counter_1_0 off_counter_0_1) (= on_counter_1_0 on_counter_0_1) (= u_1_0 u_0_1)
 /*----------------------------------------------------------*/